## Slide 1: Atmosphere in Numbers
Learning Air Quality Patterns from Satellite Data
Delhi AQI Case Study | January 2023 | 561 Hourly Observations
Data Science Research Project • Machine Learning • Urban Air Quality • Climate Change

## Slide 2: Presentation Outline
01
Problem Definition & Research Objectives
02
Dataset Description & Exploratory Data Analysis
03
Data Preprocessing & Feature Engineering
04
Machine Learning Models & Hyperparameter Tuning
05
Results, Evaluation & Comparative Analysis
06
Key Findings & Conclusions

## Slide 3: Problem Definition
The Crisis
Delhi's PM2.5 averages 266 µg/m³ — 53× WHO limit
AQI exceeds 300 (Hazardous) 63% of recorded hours
Winter atmospheric inversions trap pollutants near ground
Urban Heat Island amplifies nocturnal pollution accumulation
Research Objectives
Classify AQI categories from multi-pollutant data
Identify key pollutants driving hazardous air quality
Uncover diurnal & seasonal temporal patterns
Compare 4 ML models with hyperparameter tuning
Support climate change & UHI policy decisions
Bonus domain relevance: Urban Heat Island • Climate Change • Remote Sensing & Satellite Data

## Slide 4: Dataset Overview & EDA
561
Hourly Observations
8
Pollutant Channels
3
AQI Classes
14
Final Features
AQI Category Distribution
Hazardous (AQI > 300)
356 hrs (63.5%)
Very Unhealthy (201–300)
148 hrs (26.4%)
Unhealthy (151–200)
57 hrs (10.2%)
Key EDA Findings
PM2.5 & PM10 strongly correlated (r = 0.99)
CO peaks 02:00–05:00 (nocturnal inversion)
O₃ inversely varies with PM2.5 (photochem)
NO shows highest variance (traffic bursts)
Source: OpenWeatherMap Air Pollution API | New Delhi, India | Jan 1–24, 2023

## Slide 5: Preprocessing & Feature Engineering
✓
Missing Values
No nulls detected. Dataset is complete.
AQI Derivation
EPA PM2.5 breakpoint formula →
3-class target label
Z-Score Scaling
StandardScaler applied to all 14 features before modeling
Feature Engineering
6 new features: cyclic time, pollutant ratios, oxidant index
Engineered Features → hour_sin • hour_cos • day_of_week • co_no2_ratio • pm_ratio • oxidant_index
Total: 8 raw pollutants + 6 engineered = 14 features | 80/20 stratified train-test split | 5-fold CV

## Slide 6: Machine Learning Models
Random Forest
Robust ensemble; handles non-linearity; provides feature importance
Best Params: n_estimators: 200 • max_depth: 20 • min_samples_split: 2
Gradient Boosting
Sequential boosting captures complex interactions; high accuracy
Best Params: n_estimators: 200 • learning_rate: 0.1 • max_depth: 5
Support Vector Machine
Maximum-margin classifier; RBF kernel for non-linear boundaries
K-Nearest Neighbors
Non-parametric baseline; distance-based; interpretable
Best Params: C: 10 • kernel: RBF • gamma: scale Best Params: n_neighbors: 3 • weights: distance • metric: manhattan
All models tuned using GridSearchCV with 5-fold cross-validation (F1-weighted optimisation)

## Slide 7: Evaluation Results
Model | Accuracy | Precision | Recall | F1-Score | CV Acc
Random Forest | 1.0000 | 1.0000 | 1.0000 | 1.0000 | 0.9964
Gradient Boosting | 1.0000 | 1.0000 | 1.0000 | 1.0000 | 1.0000
SVM (RBF) | 0.9646 | 0.9661 | 0.9646 | 0.9649 | 0.8360
K-Nearest Neighbors | 0.9027 | 0.9027 | 0.9027 | 0.9005 | 0.7506
RF+GB
Best Models
100%
Test Accuracy
PM2.5
Top Feature
99.6%
RF Cross-Val
★ Gradient Boosting and Random Forest achieve perfect F1 — PM2.5 is the dominant driver of AQI classification

## Slide 8: Feature Importance & Key Patterns
Random Forest Feature Importance
PM2.5
42%
pm_ratio
4.38%
PM10
28.3%
CO
6%
co_no2_ratio
4%
oxidant_idx
3%
hour_sin
2%
NO2
1%
Diurnal Pollution Pattern
Midnight–5 AM
PEAK: Atmospheric inversion traps pollutants near surface
6–10 AM
Secondary peak: Morning traffic rush emissions
11 AM–3 PM
TROUGH: PBL deepens, dilutes surface concentrations
4–8 PM
Gradual rise: Evening traffic + cooling air
9 PM–Midnight
Rising: Nocturnal inversion begins forming again
UHI connection: Nocturnal urban warmth suppresses turbulent mixing → pollutant trapping

## Slide 9: Key Findings & Conclusions
Best Models
Gradient Boosting & Random Forest → Perfect F1 (1.00)
Critical Pollutant
PM2.5 accounts for 42% of feature importance in RF
Peak Pollution
02:00–05:00 AM due to nocturnal atmospheric inversion
Feature Engineering
PM ratio & oxidant index add predictive signal beyond raw data
Climate Relevance
UHI drives nocturnal trapping — direct link to urban climate
Future Work
GEE satellite AOD integration + LSTM multi-step forecasting
Thank You • Questions?